## Slide 1
The Basics
O2 Devices
Click on any rounded button with a cursor to navigate to other pages
Cases

## Slide 2: Respiratory Physiology
Oxygenation
Ventilation
O2
O2
O2
O2
↑ FiO2
↑ PEEP
Tidal volume (Vt)
x
Respiratory rate
↑ number or % of O2 molecules participating in gas exchange (room air is 21% FiO2)
Recruits additional alveoli during expiration to participate in gas exchange
The Basics
O2 Devices
Cases

## Slide 3: Oxygen Delivery Systems
Nasal cannula
Non-rebreather mask
Face mask (simple)
Oxymizer
High flow nasal cannula
CPAP
BiPAP
Mechanical ventilation
↑ max FiO2
100%
PEEP
Venturi mask
Oxygenation
Ventilation
The Basics
O2 Devices
Cases

## Slide 4
Effective FiO2 is dependent on pattern of breathing (minute ventilation, inspiratory flow rate) and patency of nasal passages.
E.g., with increased work of breathing, inspiratory flow rate can be > 100 L/min. This dilutes out the delivered O2 with ambient air, decreasing effective FiO2.
0
1
2
3
4
5
6
8
10
12
15
ambient air (21% FiO2)
100% FiO2
Effective FiO2
NC delivers 100% FiO2 oxygen at designated flow rates
O2 inspired from the cannula intermixes with ambient air entrained from around the device to create an effective FiO2
effective FiO2
1
2
Each 1L/min ≈ 3-4% FiO2 (↓ with ↑work of breathing)
Ideal at 2-4L/min.
Max FiO2 ~44% at 6 L/min. Higher flow rates do not significantly ↑ FiO2.
Nasal Cannula
The Basics
O2 Devices
Cases

## Slide 5
Because of venting holes and poorly fitted masks, ambient air is entrained during inspiration, diluting 100% O2 delivered to the mask.
0
1
2
3
4
5
6
8
10
12
15
ambient air (21% FiO2)
CO2
O2 is delivered at various flow rates, which collects in the face mask to create a 100 – 250 mL reservoir of 100% O2.
100% FiO2
Effective FiO2
reservoir
A reservoir collects 100% O2 and dilutes out the inspired ambient air. With nasal cannula, the reservoir is our nasopharynx (~50 mL). The larger the reservoir, the less ambient air is entrained with every breath.
Simple Face Mask
1
Maximal FiO2 delivered ~ 60-70% (with normal breathing)
  5-6 L/min ≈ 40% FiO2
  6-7 L/min ≈ 50% FiO2
  7-8 L/min ≈ 60% FiO2
The reservoir ↓ the entrained ambient air with each breath
The mask collects expired CO2. High flow rates of > 6 L/min are needed to wash out the CO2 to prevent rebreathing
2
3
The Basics
O2 Devices
Cases
Notes: Smart, DR. Oxygen Therapy. In: Cameron, P, et al., eds. Textbook of Adult Emergency Medicine. Fourth Edition. 2-15. Churchill Livingstone, Elsevier Ltd.

## Slide 6
0
1
2
3
4
5
6
8
10
12
15
ambient air (21% FiO2)
100% FiO2
35% FiO2
35
CO2
The Venturi device, entrains ambient air and mixes it with 100% O2 – delivering a fixed flow rate and FiO2 to the mask.
Venturi device
Venturi Mask
1
Higher desired FiO2 requires lower flow rates
  Desired 35% FiO2 → ~45 L/min
    Desired 60% FiO2 → ~ 30 L/min flow
Maximum FiO2 of ~60% with flow rates up to 60 L/min
  Useful for providing set FiO2 to patients with a variable breathing pattern
2
The Basics
O2 Devices
Cases

## Slide 7
0
10
20
30
40
50
60
PEEP
High Flow Nasal Cannula
Adjustable FiO2 and flow rate.
Maximum flow rate is ~ 60 L/min and maximum effective FiO2 is near 100%.
FiO2(%)
0
100
60
40
20
80
Humidifier
Thicker nasal cannula prongs, which occlude the nasal passages, combined with the high flow rates, generate small amounts of PEEP (~ 3-5 cm H2O).
Thick nasal cannula prongs
Set FiO2
PEEP
Trachea
High flow rates of O2 wash out the nasopharynx and upper airways with the delivered O2, creating an oxygen reservoir. This also ↓ CO2 rebreathing and dead space.
1
Higher flow rates delivered are able to match higher inspiratory flow rates in patients with ↑ work of breathing and minute ventilation.
2
3
The Basics
O2 Devices
Cases

## Slide 8
0
1
2
3
4
5
6
8
10
12
15
Non-rebreather Mask
ambient air (21% FiO2)
CO2
100% FiO2
One way valve
(inhalation)
One way valve
(exhalation)
Reservoir bag
A reservoir bag that varies from 600 mL – 1.5 L. The bag must be inflated to create a reservoir! Flow rates of >10 L/min are required to fill the bag.
A one-way inhalation valve between the mask and reservoir bag allows O2 to flow from the tubing → reservoir bag → mask but does not allow exhaled CO2 to re-enter the bag.
One-way exhalation valves let out exhaled CO2.
1
One-way valves control the flow of O2 and CO2 to allow the patient to preferentially breathe 100% FiO2 from the reservoir bag and expel CO2 into the environment.
2
Maximum effective FiO2 of 75 – 90% at flow rates of 12 – 15 L/min.
Rescue form of oxygen only!!
3
The Basics
O2 Devices
Cases

## Slide 9
0
1
2
3
4
5
6
8
10
12
15
Oxymizer
Oxymizers contain an additional 20 mL reservoir in a pendant or mustache“ shape.
Oxymizer reservoir
ambient air (21% FiO2)
100% FiO2
*maximum values noted are reported from manufacturing details
Dumont, CP & Tiep, BL. 2002. Using a Reservoir Nasal Cannula in Acute Care. Critical Care Nurse. 22(4): 41-46.
Tiep, BL & Belman, MJ. 1985, A new Pendant Storage Oxygen-conserving Nasal Cannula. CHEST. 87: 381-383.
reservoir
A reservoir collects 100% O2 and dilutes out the inspired ambient air. With nasal cannula, the reservoir is our nasopharynx (~50 mL). The larger the reservoir, the less ambient air is entrained with every breath.
1
The additional reservoir allows ↑ flow rates to be delivered more comfortably and ↑ effective FiO2 for the same flow rate as compared to nasal cannula.
  Max flow rates reported at 20 L/min, but in practice, ~12-15 L/min
2
Effective FiO2 is affected by work of breathing
  Max FiO2 reported is > 80%, but in practice, likely lower
The Basics
O2 Devices
Cases

## Slide 10
IPAP recruits additional alveoli during inspiration → ↑ Vt
Pressure
time
Pressure
time
Affects oxygenation (PEEP)
Constant pressure through inspiration and expiration (aka PEEP)
CPAP
BiPAP
expiration
inspiration
Affects oxygenation (PEEP) and ventilation (tidal volume)
Noninvasive Positive Pressure Ventilation
EPAP is PEEP.
↑EPAP = ↑ PEEP.
EPAP
IPAP
Allows for titration of both FiO2 and PEEP
The greater the difference between IPAP and EPAP (or ΔPAP), the greater the Vt
The Basics
O2 Devices
Cases
NIPPV Effects
Indications

## Slide 11
Noninvasive Positive Pressure Ventilation
Physiologic Effects
↓ RV preload
↑ intrathoracic P → pressure gradient between thoracic and abdominal aorta → ↓ effort required by LV to eject blood out of the heart
THORAX
ABDOMEN
↑ Pressure
↑ Pressure
RV
LV
↓ LV preload
↑ intrathoracic P → ↑ resistance to venous return to the R heart
1
↑ intrathoracic P → ↑ resistance of blood flow out of the RV (≈ ↑ in RV afterload) → ↓ blood flow to L side of the heart
2
3
↓ LV afterload
The Basics
O2 Devices
Cases
NIPPV Effects
Indications

## Slide 12
Noninvasive Positive Pressure Ventilation
Indications in acute respiratory failure
The Basics
O2 Devices
Cases
NIPPV Effects
Indications
CPAP
BiPAP
Acute cardiogenic pulmonary edema
Immunocompromised patients
Post-operative respiratory failure
Post-extubation respiratory failure
Palliative
COPD exacerbation with hypercapnic respiratory failure
Neuromuscular disease
ACUTE
RESPIRATORY FAILURE
OSA/ OHS
CHRONIC
Contra-indications
Inability to wear a mask (facial trauma)
Inability to pull off a mask (AMS, paralysis)
Active nausea/vomiting, copious secretions
Recent esophageal or tracheal surgery

## Slide 13
The Basics
O2 Devices
Cases
Case 1
64 yo with R sided renal cell carcinoma present for a R nephrectomy. On POD5, they develop acute onset SOB.
VS: T 37.1C, HR 140, BP 90/60, RR 28, SaO2 82% on RA.
How would you improve their SaO2?
How would you improve their SaO2?
What is your next step in management?
Trial of nasal cannula can be used for mild-moderate hypoxemia
They can be escalated to an oxymizer, Venturi mask or HFNC
Intubation and mechanical ventilation. There is hypoxemic and hypercarbic respiratory failure despite max FiO2. PEEP is needed to ↑ PaO2. BiPAP is contraindicated with AMS. Other contraindications to NIPPV: facial trauma, copious secretions, nausea/vomiting, hemodynamic instability.
Case 2
74 yo with a history of COPD presents with a COPD exacerbation.
VS: T 37.1C, HR 120, BP 160/60, RR 32, SaO2 82% on RA.
PE: Sleepy but easily arouses. Diffuse wheezing.
CXR is clear. ABG shows 7.21/72/45/28.
Case 3
56 yo with HFrEF is admitted with a HFrEF exacerbation. CXR shows diffuse bilateral alveolar infiltrates.
VS: T 36.5C, HR 110, BP 160/80, RR 32, SaO2 75% on RA.
How would you improve their SaO2?
How would you adjust their BiPAP settings?
What if the ABG showed 7.35/45/55/28?
What if the ABG showed 7.30/60/55/28?
BiPAP is needed for hypoxemic and hypercarbic respiratory failure.
Increase the IPAP. There is persistent hypercarbic respiratory failure. To improve ventilation, ↑ the ΔPAP.
There is persistent hypoxemia (PaO2 55) but respiratory acidosis/ hypercapnia is resolved (7.35/45). Hypoxemia can be addressed by ↑ FiO2 or EPAP/IPAP proportionately (e.g., 12/7)
There is persistent hypoxemia (PaO2 55) and hypercapnia (7.30/60). Options include:
↑ IPAP alone + ↑ FiO2. E.g. 12/5, 50% FiO2
Or ↑ EPAP and ΔPAP. E.g., 15/7.
How would you improve their SaO2?
What is your next step in management?
Start CPAP. They have persistent hypoxemia despite near max FiO2. Additionally, acute cardiogenic pulmonary edema is a strong indication for NIPPV.
They progressively desaturate and are now on 6L NC with SaO2 89%.
On POD7, they are on HFNC 100% FiO2, 60 L/min. RR is 24 and shallow, SaO2 86%. They are obtunded and difficult to arouse. ABG shows 7.21/72/45/20.
They are placed on BiPAP of 10/5, 35% FiO2. Repeat ABG shows 7.30/60/79/28.
Given severity of hypoxemia, consider a non-rebreather to quickly improve oxygenation.
On non-rebreather, SaO2 improves to 89%, RR is now 28. ABG shows 7.46/29/59/24.

## Slide 14
Maximum FiO2
100%
40%
60%
80%
Range of Flow Rates (L/min)
80
60
40
20
10
8
6
4
2
0
NON-REBREATHER MASK
MAXIMUM FiO2 AND FLOW RATES FOR OXYGEN DELIVERY DEVICES
HIGH FLOW NASAL CANNULA
OXYMIZER
SIMPLE FACE MASK
NASAL CANNULA
VENTURI MASK

## Slide 15
Oxygen Delivery — 2022–25 Context Update
The device physiology, NIPPV mechanics, and indications are timeless and verified current (June 2026). The items below add modern evidence; standing teaching unchanged.
HFNC first-line for acute hypoxemic respiratory failure: ESICM ARDS 2023 recommends HFNC over conventional oxygen in non-intubated AHRF to reduce intubation — EXCEPT cardiogenic pulmonary edema and COPD exacerbation, where NIPPV (CPAP/BiPAP) is preferred. Consistent with FLORALI (Frat, NEJM 2015).
Monitor HFNC with the ROX index = (SpO2/FiO2) ÷ RR. ROX ≥4.88 at 2/6/12 h predicts HFNC success; a low or falling ROX flags impending failure — escalate, do not delay intubation (Roca, AJRCCM 2019).
Awake prone positioning is a recommended adjunct for non-intubated patients with COVID-related hypoxemic AHRF on HFNC/NIPPV — reduces intubation (strong rec, 2023 rapid practice guideline); trial 15 min, continue if tolerated.
CPAP vs HFNC in COVID AHRF (RECOVERY-RS, JAMA 2022): CPAP reduced the intubation/death composite vs conventional oxygen; HFNC did not differ. HFNC and NIV are otherwise similarly effective at avoiding intubation in AHRF (2023 meta-analysis).

## Slide 16
Take-Home Points
1. Hypoxemia is corrected by raising FiO2 or adding PEEP. Most ward devices (nasal cannula, simple/Venturi/NRB masks, oxymizer) adjust only FiO2; effective FiO2 falls as work of breathing/inspiratory flow rises.
2. HFNC delivers high, matched flow with finely titratable FiO2 (up to ~100%) and a small, non-adjustable PEEP (~3-5 cm H2O); it improves oxygenation, work of breathing, and minute ventilation.
3. NRB is a RESCUE device only — de-escalate once stable. Venturi gives a precise set FiO2 for variable breathing patterns.
4. CPAP = oxygenation only (PEEP). BiPAP (IPAP−EPAP = ΔPAP) adds ventilation → use for hypercapnic failure. Both unload the heart (↓ RV/LV preload, ↓ LV afterload) — strong in acute cardiogenic pulmonary edema; BiPAP for COPD hypercapnic failure.
5. First-line for AHRF is HFNC (except cardiogenic edema and COPD); add awake proning; track the ROX index and escalate early.

## Slide 17
Attribution & Optimization Notes
Original lesson: “Oxygen Delivery Systems,” TeachIM.org (updated Oct 2021).
Author: Yilin Zhang MD (Valley Medical Center).
Source URL: teachim.org/teaching_material/oxygen-delivery-systems/
License: Creative Commons Attribution-NonCommercial 4.0 International (CC BY-NC 4.0). Non-commercial educational use only.
Corrections made (this edit, all single-run XML, animations preserved): (1) HFNC slide PEEP unit "3-5 mm H2O" -> "3-5 cm H2O" (airway pressures are cm H2O); (2) Case 3 spelling "non-rebreathrer" -> "non-rebreather"; (3) Oxymizer citation page range "381=383" -> "381-383".
Context added (source-cited): ESICM ARDS 2023 (HFNC first-line for AHRF); ROX index (Roca AJRCCM 2019); awake-proning 2023 rapid practice guideline; RECOVERY-RS (JAMA 2022). FLORALI/Hernandez already cited on deck.
No companion handout is published for this lesson (single interactive board). Medical content should be clinician-reviewed before teaching.