## Slide 1
Key Outputs
Definitions
Peak P Alarm
Assessing Pulmonary Mechanics in a Ventilated Patient
Cases
Graphics created with biorender.com
Summary

## Slide 2
Peak pressure (Ppeak)
Plateau pressure (Pplateau)
Driving pressure (Pdriving)
Volume-Targeted Modes
Pressure-Targeted Modes
Key Parameters?
Key Outputs to Monitor Pulmonary Mechanics
Volume-Targeted Modes
Pressure-Targeted Modes
Key Parameters?
Peak pressure (Ppeak)
Plateau pressure (Pplateau)
Driving pressure (Pdriving)
Ppeak
Pplateau
Pdriving = Pplateau - PEEP
PEEP
Time
Pressure
Inspiratory hold
Key Outputs
Definitions
Peak P Alarm
Cases
Summary
VE = RR x VT
Minute ventilation (VE)
Tidal volume (VT)

## Slide 3
Opposition to airflow through the system (tubing, airways)
Typically, <10.
Stiffness of respiratory system (lungs, pleural, chest wall, abdomen)
Normally, pressure needed to achieve 4-6 cc/kg is <10
Ppeak
Pplateau
PEEP
Time
Pressure
Inspiratory hold
R ∝ Ppeak – Pplateau
RESISTANCE
COMPLIANCE
Pdriving = Pplateau – PEEP
RESISTANCE
COMPLIANCE
Inspiratory hold
Pplateau
Key Outputs
Definitions
Peak P Alarm
Ppeak
Pplateau
Pdriving
Definitions
Cases
Summary

## Slide 4
Stiffness of respiratory system (lungs, pleural, chest wall, abdomen)
Normally, pressure needed to achieve 4-6 cc/kg is <10
Opposition to airflow through the system (tubing, airways)
Typically, <10.
↑ resistance → ↑ peak pressure
Ppeak
PEEP
Time
Pressure
~Resistance
RESISTANCE
COMPLIANCE
What Influences Peak Pressures?
~
Inspiratory hold
1
Inspiratory flow rate/ pattern
Key Outputs
Definitions
Peak P Alarm
Ppeak
Pplateau
Pdriving
1
2
2
3
3
4
4
Cases
Summary

## Slide 5
Time
Pressure
What Influences Plateau Pressure?
Inspiratory hold
Pplateau
Key Outputs
Definitions
Peak P Alarm
Ppeak
Pplateau
Pdriving
Because plateau pressure is measured during an inspiratory hold, there is NO AIR FLOW and thus no resistance in the system.
Cases
Summary

## Slide 6
Pplateau
PEEP
Time
Pressure
What Influences Driving Pressure?
Inspiratory hold
Key Outputs
Definitions
Peak P Alarm
Ppeak
Pplateau
Pdriving
Pdriving = Pplateau – PEEP
Cases
Summary
Stiffness of respiratory system (lungs, pleural, chest wall, abdomen)
Normally, pressure needed to achieve 4-6 cc/kg is <10
COMPLIANCE

## Slide 7
Responding to Peak Pressure Alarm
Step 1
Step 2
Key Outputs
Definitions
Step 3
STEP 1: ESTABLISH URGENCY
Check vitals
PCO2 (on ABG)
VT and VE (on vent)
↓O2, VT, VE
or
↑PCO2
O2 > 88%
VT > 4cc/kg ↓↓VE
Get HELP!
Proceed
Peak P Alarm
Cases
Summary

## Slide 8
Time
Pressure
STEP 2: ASSESS RESISTANCE
Differential?
Peak Pressure ↑
Plateau Pressure ↔
Ppeak – Pplateau > 10 suggests resistance problem
Step 1
Step 2
Step 3
STEP 1: ESTABLISH URGENCY
Ppeak
Pplateau
Baseline
New condition
Differential?
Ppeak
Pplateau
Mucus plugging
Bronchospasm
Kinked tubing or ETT
Action?
Proceed if:
Hemodynamically stable
O2 > 88%
VT > 4cc/kg
↓↓VE
~R >10
Peak P Alarm
Key Outputs
Definitions
Responding to Peak Pressure Alarm
Summary
Biting ETT
Cases

## Slide 9
Mucus plugging
Bronchospasm
Kinked tubing or ETT
Check tubing
Suction
Bronchodilators
STEP 1: ESTABLISH URGENCY
Proceed if:
Hemodynamically stable
O2 > 88%
VT > 4cc/kg
↓↓VE
Responding to Peak Pressure Alarm
STEP 2: ASSESS RESISTANCE
Differential?
Peak Pressure ↑
Plateau Pressure ↔
Ppeak – Pplateau > 10 suggests resistance problem
Action?
Biting ETT
Step 1
Step 2
Step 3
Peak P Alarm
Definitions
Summary
Cases
Key Outputs
↑ analgesia/ sedation

## Slide 10
Step 1
Step 2
Step 3
STEP 1: ESTABLISH URGENCY
Proceed if:
Hemodynamically stable
O2 > 88%
VT > 4cc/kg
↓↓VE
STEP 3: ASSESS COMPLIANCE
Differential?
Peak Pressure ↑
Plateau Pressure ↑
Pdriving > 10 suggests compliance problem
Action?
Differential?
Action?
Alveolar filling
ARDS
Pulmonary edema
Pneumonia
DAH
Time
Pressure
Ppeak
Pplateau
Baseline
New condition
Ppeak
Pplateau
Pdriving >10
Peak P Alarm
Key Outputs
Definitions
Responding to Peak Pressure Alarm
Summary
STEP 2: ASSESS RESISTANCE
Differential?
Bronchospasm
Kinked tubing
Mucus plug
Peak Pressure ↑
Plateau Pressure ↔
Ppeak – Pplateau > 10 suggests resistance problem
PTX
Abdominal distention
Atelectasis/ lobar collapse
Pleural effusion
Alveolar collapse

## Slide 11
STEP 1: ESTABLISH URGENCY
Proceed if:
Hemodynamically stable
O2 > 88%
VT > 4cc/kg
↓↓VE
STEP 3: ASSESS COMPLIANCE
Differential?
Peak Pressure ↑
Plateau Pressure ↑
Pdriving > 10 suggests compliance problem
Action?
Alveolar filling
ARDS
Pulmonary edema
Pneumonia
DAH
Responding to Peak Pressure Alarm
STEP 2: ASSESS RESISTANCE
Differential?
Bronchospasm
Kinked tubing
Mucus plug
Peak Pressure ↑
Plateau Pressure ↔
Ppeak – Pplateau > 10 suggests resistance problem
PTX
Abdominal distention
Atelectasis/ lobar collapse
Pleural effusion
Alveolar collapse
Evaluate for underlying pathology
  Exam
  CXR
  Abdominal XR
Treat underlying pathology
Step 1
Step 2
Step 3
Peak P Alarm
Key Outputs
Definitions
Summary

## Slide 12
Pressure
Baseline
New condition
Ppeak
Pplateau
Differential?
Bronchospasm
Kinked tubing
Mucus plug
STEP 1: ESTABLISH URGENCY
Proceed if:
Hemodynamically stable
O2 > 88%
VT > 4cc/kg
VE > 3L/min
STEP 3: ASSESS COMPLIANCE
Peak Pressure ↑
Plateau Pressure ↑
Pdriving > 10 suggests compliance problem
Pdriving >10
Differential?
Intrapulmonary process
Pleural effusion
Abdominal distention
New condition
Ppeak
Pplateau
Key Outputs
Definitions
Peak P Alarm
Summary
~R >10
Responding to Peak Pressure Alarm
Peak Pressure ↑
Plateau Pressure ↔
Ppeak – Pplateau > 10 suggests resistance problem
Cases
STEP 2: ASSESS RESISTANCE

## Slide 13
Cases
Case 1
65 yo is intubated in the ICU for COVID pneumonia. You are called to assess gradually rising Ppeak, which increased from ~ 35 to consistently 40. He is on assist control, volume control mode of ventilation. Settings are: 70% FiO2, PEEP 12, RR 20, Vt 5 cc/kg (450 cc). The patient is currently deeply sedated and paralyzed.
Vitals: T 37C, BP 110/57, HR 93, RR 24, SaO2 97%. Vt is 450 cc.
What is your first step in evaluation?
Establish urgency.. Vitals and oxygenation are stable. VE (RR x Vt) is acceptable. This patient is stable.
What is your next step in evaluation?
Assess for a resistance and/or compliance problem by obtaining a plateau pressure. This can be done with an inspiratory hold.
Is there a resistance problem?
No. Resistance is proportional to Peak – Plateau. A difference >10 suggests high resistance. Here, 40 – 38 = 2, which is low.
Is there a compliance problem?
Yes. Compliance is inversely proportional to the driving pressure (Plateau – PEEP). The driving pressure (38 – 12) is 26, which is elevated. This suggests low compliance.
What is your differential for the low compliance?
Alveolar process - pulmonary edema, worsening pneumonia, atelectasis
Restricted expansion - pleural effusions
Given slow rise in peak pressure, a pneumothorax or lobar collapse are less likely.
What are your next steps in evaluation?
Get additional history. Perform a targeted physical exam. Obtain a CXR or bedside US and ABG to evaluate for new intrapulmonary processes. CBC, BMP, BNP.
…Exam reveals soft abdomen, diffuse crackles. CXR shows worsening bilateral interstitial and alveolar infiltrates. CBC shows worsening leukocytosis. pH 7.34/45/82/24 on 70% FiO2.
What are the most likely diagnosis?
Worsening parenchymal lung disease, which could include from ARDS or superimposed bacterial infection.
1
2
…Plateau pressure is 38 cmH2O.
Key Outputs
Definitions
Peak P Alarm
Summary

## Slide 14
Case 2
25 yo with asthma presents with acute hypercarbic and hypoxemic respiratory failure from an asthma exacerbation. They are intubated and placed on volume-targeted mode of ventilation with FiO2 of 70%, PEEP 5, Vt 350 cc (6cc/kg), RR 24. One hour after intubation, they become progressively hypotensive and hypoxemic. BPs are 100s/60s, RR 30, SaO2 92%, HR 120s. The ventilator is alarming for high peak pressures of 38 cm H2O. Vt delivered is 300 cc.
What is the urgency of the situation?
Vitals and oxygenation are stable. Proceed with assessment. Obtain ABG to assess pCO2 and pH if not done recently.
What is your next step in management?
Inspiratory hold to measure the plateau P. This helps differentiate a resistance vs. compliance issue.
Is there a resistance or compliance problem?
Resistance. Peak – Plateau is = 15. There is NO compliance issue. Plateau is <30 and driving P (Plateau – PEEP) is <10.
What is the most likely diagnosis?
How would you manage this?
Is there a resistance or compliance problem?
The patient’s BPs are trending down. Call for help!
There is a compliance issue. Plateau P - PEEP >10.
There is NO resistance issue. Peak – Plateau <10.
What is the most likely diagnosis?
AutoPEEP or pneumothorax.
…The plateau P is 20. ABG shows 7.25/60/95/24.
Key Outputs
Definitions
Peak P Alarm
…After escalating therapy and ↑ RR to address the acidosis, the Peak P is still 35. Plateau P ↑ to 30. RR is 35, PEEP 12. BPs 80s/60s.
Bronchospasm and airway inflammation.
Escalate bronchodilator ± steroid therapy. Consider IV magnesium if no improvement with aggressive bronchodilators.
What is your next step in evaluation/management?
Slow RR to ↑ expiration time (as long as pH allows). Listen for bilateral breath sounds. CXR or POCUS to evaluate for PTX.
…The patient goes into cardiac arrest. POCUS rules out PTX.
What is your next step in management?
Call a Code Blue. Disconnect from ventilator and allow for long exhalation. Start ACLS and use manual bagging (RR 8-10).
Summary
Cases
1
2

## Slide 15
Pulmonary Mechanics — 2023–25 Context Update
Core mechanics teaching (resistance, compliance, peak/plateau/driving pressure, the high-peak-pressure algorithm) is timeless physiology — verified current June 2026. The items below add context, not corrections.
Driving pressure (ΔP = Pplateau − PEEP) is the mechanic most tightly linked to ARDS survival. Keep ΔP ≤ 14–15 cm H₂O — risk rises stepwise above this even when Vt ≤6 mL/kg and Pplat ≤30 (Amato, NEJM 2015; LUNG SAFE).
Lung-protective targets unchanged: Vt 4–6 mL/kg ideal body weight, Pplateau <30 cm H₂O, PEEP >5 (ARDSNet NEJM 2000; ATS/ESICM/SCCM 2017; ESICM ARDS 2023).
ESICM ARDS 2023 / Global (new) ARDS definition 2024: SpO₂/FiO₂ ≤315 (when SpO₂ ≤97%) may define ARDS, lung ultrasound is an accepted imaging modality, and HFNO is included as a recognized support category — broadens who you will be troubleshooting on the vent.
Bedside rule of thumb retained: normal resistance Ppeak−Pplateau <10; normal compliance driving pressure <10 cm H₂O for a 4–6 mL/kg breath.

## Slide 16
Take-Home Points
1. Peak and plateau are the key outputs in volume-targeted modes. Peak pressure reflects resistance + compliance + PEEP + inspiratory flow; plateau (measured on an inspiratory hold) should be <30 cm H₂O.
2. For a high-peak-pressure alarm: (1) establish urgency at the bedside, then (2) get a plateau pressure and decide resistance vs compliance vs both.
3. Resistance ∝ Ppeak − Pplateau. >10 cm H₂O = resistance problem → kinked/bitten/blocked tube, mucus plug, bronchospasm. Fix: inspect tubing, suction, bite block/sedation, bronchodilators.
4. Compliance ∝ 1/driving pressure (Pplateau − PEEP). Driving pressure >10 (or Pplateau >30) = compliance problem → alveolar filling (edema, ARDS, pneumonia, DAH) or collapse (atelectasis, PTX, effusion, abdominal distention). Keep ΔP ≤14–15.
5. They can co-exist — and a falling BP, SpO₂, or VE turns troubleshooting into an emergency: call for help and bump FiO₂ to 100% first.

## Slide 17
Attribution & Optimization Notes
Original lesson: “Ventilators Part 2 — Assessing Pulmonary Mechanics in a Ventilated Patient,” TeachIM.org (updated Apr 2023).
Authors: Kaitlyn McLeod MD, David Scudder MD; Section Editor Trevor Steinbach MD; Executive Editor Yilin Zhang MD.
Source URL: teachim.org/teaching_material/ventilators-part-2-assessing-pulmonary-mechanics-in-a-ventilated-patient/
License: Creative Commons Attribution-NonCommercial 4.0 International (CC BY-NC 4.0). Non-commercial educational use only.
Correction made (this edit): Case 1 driving-pressure arithmetic “(38 − 12) is 14” → “is 26” (plateau 38, PEEP 12; conclusion “elevated / low compliance” unchanged). All original animations, graphics, and slide order preserved.
Human review: Case 2 numbers are internally inconsistent (Peak−Plateau and driving-pressure values do not reconcile with the stated peak/plateau/PEEP) — left unchanged pending author confirmation.
Companion files: Teaching guide (Vent-mechanics-4.11.docx) and Learner handout (Ventilators-Hand-out.pdf) — reviewed, no changes. Added context source-cited: Amato NEJM 2015; ARDSNet NEJM 2000; ATS/ESICM/SCCM 2017; ESICM ARDS 2023; Global ARDS definition 2024. Medical content should be clinician-reviewed before teaching.